IBEX Goat Herder 4 Oct 17

The Apogee Tracking Contact for Orbit# 382 was nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Wednesday, October 04, 2017	277	0800	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	935	Apogee	2ksps	175 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

670	4	1435	34	0	0

VC 2 Write Pointer Start	59690	VC 2 Write Pointer End	59757

VC 2 Read Pointer Start	49953	VC 2 Read Pointer End	49953

Orbit# 382 Apogee Tracking Contact

@FMI_SetDownlink (40k)

CAR# 935 Upload Orbit# 383 APL18 Contact 1.IBEX_2017_281_o0383a_APL18_v001.scr (59-65)

IBEX Orbit# 382 APOGEE Target Vectors 4 Oct 17

J2000	Spin Axis

ECI X	-0.989754

ECI Y	-0.131294

ECI Z	-0.056117

Precession Maneuver

MPS Diff	0.787	deg

*MPS Diff should be < 1.5*

0.45058000	ActNor.EstInrToBdy[0]

-0.57011900	ActNor.EstInrToBdy[1]

-0.35139100	ActNor.EstInrToBdy[2]

0.59031000	ActNor.EstInrToBdy[3]

1191140000.000	ActNor.EstTime

Right Ascension - RA	187.556	deg

Declination - DEC	-3.217	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.091	deg

MPS Generated APOGEE Target Vectors

MPS Cmd Vector X	-0.988500000

MPS Cmd Vector Y	-0.134318000

MPS Cmd Vector Z	-0.069478000

CSS Angle TLM	0.455425

CSS Sun-Pointing Angle	0.91085

29 Sept17 @1300

CSS Angle TLM	0.459275

CSS Sun-Pointing Angle	0.91855

04 Oct 17 @0800

Pre-Burn

Thruster 1	3392	29 Sept17 @1300

Thruster 2	3328

Thruster 3	3568

Thruster 4	3632

Post-Burn

Thruster 1	3664	04 Oct 17 @0800

Thruster 2	3600

Thruster 3	3872

Thruster 4	3936

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608