IBEX Goat Herder  23 Oct 17

The Apogee Tracking Contact for Orbit# 384 was nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, October 23, 2017	296	0700	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	938	45 desc	2ksps	170 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

608	3	1430	34	0	0

VC 2 Write Pointer Start	38992	VC 2 Write Pointer End	39054

VC 2 Read Pointer Start	27743	VC 2 Read Pointer End	27743

Orbit# 384 Apogee Tracking Contact

@FMI_Set Downlink (40k)

CAR# 938 Upload Orbit# 385 ATS  1.IBEX_2017_300_o0385a_v001.scr(463-545)

@FTG_DumpBAckorbit(from start,0,0,0,0)

IBEX Orbit# 385 APOGEE Target Vectors 23 Oct 17

J2000	Spin Axis

ECI X	-0.895109

ECI Y	-0.409515

ECI Z	-0.176285

Precession Maneuver

MPS Diff	0.811	deg

*MPS Diff should be < 1.5*

0.74301100	ActNor.EstInrToBdy[0]

-0.18994100	ActNor.EstInrToBdy[1]

-0.49927700	ActNor.EstInrToBdy[2]

0.40321200	ActNor.EstInrToBdy[3]

1192780000.000	ActNor.EstTime

Right Ascension - RA	204.584	deg

Declination - DEC	-10.153	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.632	deg

MPS Generated APOGEE Target Vector

MPS Cmd Vector X	-0.891339000

MPS Cmd Vector Y	-0.411724000

MPS Cmd Vector Z	-0.189730000

CSS Angle TLM	0.49218

CSS Sun-Pointing Angle	0.98436

17 Oct 17 @2300

CSS Angle TLM	0.716235

CSS Sun-Pointing Angle	1.43247

23 Oct 17 @0700

Pre-Burn

Thruster 1	4560	17 Oct 17 @2300

Thruster 2	4464

Thruster 3	4800

Thruster 4	4896

Post-Burn

Thruster 1	4832	23 Oct 17 @0700

Thruster 2	4736

Thruster 3	5104

Thruster 4	5200

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608