IBEX Goat Herder  27 Oct 17

The Perigee contacts for Orbit# 384 were nominal for command/telemetry and the inertial maneuver successful.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Friday, October 27, 2017	300	1200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	939	11 asc	64ksps	180 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1666	5	1445	32	0	0

VC 2 Write Pointer Start	48371	VC 2 Write Pointer End	48408

VC 2 Read Pointer Start	48182	VC 2 Read Pointer End	48182

Orbit# 384 Perigee Tracking Contact

CAR# 939 Upload Orbit# 386 ATS 1. IBEX_2017_309_o0386a_v001.scr(643-739)

reset_master_timer.scr

ops_set_sc_time.scr

@ACT_ResetTaskRawFAiled(AC_FDC)

@FMI_SetDownlink(64ksps)

@FTG_DumpBAckOrbit(from start,0,0,0,0)

IBEX Orbit# 384 PERIGEE Target Vectors  27 Oct 17

J2000	Spin Axis

ECI X	-0.856079

ECI Y	-0.475302

ECI Z	-0.203021

Precession Maneuver

MPS Diff	0.770	deg

*MPS Diff should be < 1.5*

-0.63731300	ActNor.EstInrToBdy[0]

-0.44197600	ActNor.EstInrToBdy[1]

0.62813700	ActNor.EstInrToBdy[2]

0.06271730	ActNor.EstInrToBdy[3]

1193140000.000	ActNor.EstTime

Right Ascension - RA	209.039	deg

Declination - DEC	-11.714	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.148	deg

MPS Generated PERIGEE Target Vectors

MPS Cmd Vector X	-0.853101000

MPS Cmd Vector Y	-0.474889000

MPS Cmd Vector Z	-0.216099000

PERIGEE Sun Angle/Thruster Counts

CSS Angle TLM	0.716235

CSS Sun-Pointing Angle	1.43247

23 Oct 17 @0700

CSS Angle TLM	0.673476

CSS Sun-Pointing Angle	1.346952

27 Oct 17 @1200

Pre-Burn

Thruster 1	4832	23 Oct 17 @0700

Thruster 2	4736

Thruster 3	5104

Thruster 4	5200

Post-Burn

Thruster 1	5104	27 Oct 17 @1200

Thruster 2	5008

Thruster 3	5408

Thruster 4	5504

Number of Pulses

Thruster 1	272

Thruster 2	272

Thruster 3	304

Thruster 4	304

Thruster Pairs

Thruster 1 & 2	544

Thruster 3 & 4	608