IBEX Goat Herder  2 Nov 17

The Apogee Tracking contact was nominal for command/telemetry and the sun maneuver successful

The Apogee contact was extended to exercise all three MAESTRO servers and CMD workstations.

- AOS with MAESTRO03/ibex-3 (primary)

- Switch to MAESTRO02/ibex-2 (back-up)

- LOS with MAESTRO01/ibex-1 (testing)

The command/telemetry testing was successful and data files currently being processed.

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Thursday, November 02, 	306	0200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	43 desc	2ksps	162 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1021	13	1448	28	0	0

VC 2 Write Pointer Start	60142	VC 2 Write Pointer End	60247

VC 2 Read Pointer Start	48182	VC 2 Read Pointer End	48182

Orbit# 385 Apogee Tracking Contact

@FMI_SetDownlink(40k)

stx,off(2017/11:02:03:02:00)

@FCH_DelTimedCmd(517,stx-off  2017/11:02:02:35:00

@FTG_DumpBAckorbit(from start,0,0,0,0)

stx,off

IBEX Orbit# 385 APOGEE Sun Maneuver

CSS Angle TLM	0.67346

CSS Sun-Pointing Angle	1.34692

27 Oct 17 @1200

CSS Angle TLM	0.844646

CSS Sun-Pointing Angle	1.689292

02 Nov 17 @0200

Pre-Burn

Thruster 1	5104	27 Oct 17 @1200

Thruster 2	5008

Thruster 3	5408

Thruster 4	5504

Post-Burn

Thruster 1	5472	02 Nov 17 @0200

Thruster 2	5344

Thruster 3	5920

Thruster 4	6048

Number of Pulses

Thruster 1	368

Thruster 2	336

Thruster 3	512

Thruster 4	544

Thruster Pairs

Thruster 1 & 2	704

Thruster 3 & 4	1056