IBEX Goat Herder  5 Nov 17

The Perigee Contacts for Orbit# 385 were nominal for commands/telemetry and the sun maneuver successful

The e SSR read and write pointers were reset

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, November 05, 2017	309	0900	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	940	11 desc	320ksps	178 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1551	1	0	0	19859	0

VC 2 Write Pointer Start	2503	VC 2 Write Pointer End	6543

VC 2 Read Pointer Start	48182	VC 2 Read Pointer End	6500

IBEX Orbit# 385 Perigee SSR_Dump Contact

reset_master_timer.scr

SSR_Dump.scr (new,RESET_PNTRS 6500)

CAR# 940 Upload 	Orbit# 387 ATS 1.IBEX_2017_318_o0387a_v001(835-920) 2.IBEX_2017_318_o0387a_APL18_v001(921-927)

STX,off

IBEX Orbit# 387 PERIGEE Target Vectors

CSS Angle TLM	0.844646

CSS Sun-Pointing Angle	1.689292

02 Nov 17 @0200

CSS Angle TLM	0.39017

CSS Sun-Pointing Angle	0.78034

05 Nov 17 @0900

Pre-Burn

Thruster 1	5472	02 Nov 17 @0200

Thruster 2	5344

Thruster 3	5920

Thruster 4	6048

Post-Burn

Thruster 1	5648	05 Nov 17 @0900

Thruster 2	5520

Thruster 3	6272

Thruster 4	6400

Number of Pulses

Thruster 1	176

Thruster 2	176

Thruster 3	352

Thruster 4	352

Thruster Pairs

Thruster 1 & 2	352

Thruster 3 & 4	704

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Sunday, November 05, 2017	309	1500	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	11 asc	64ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

834	11	1450	28	0	0

VC 2 Write Pointer Start	0	VC 2 Write Pointer End	6686

VC 2 Read Pointer Start	0	VC 2 Read Pointer End	6500

Orbit# 385 Perigee Tracking Contact

@FMI_SetDownlink (40k)

@FTG_DumpBAckorbit(from start,0,0,0,0)

stx,off