IBEX Goat Herder  11 Nov 17

The Apogee tracking contact for Orbit# 386 was nominal for command/telemetry and the inertial maneuver successful

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, November 11, 2017	315	0200	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	44desc	2ksps	187 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

217	2	0	0	0	0

VC 2 Write Pointer Start	18837	VC 2 Write Pointer End	18893

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	6500

Orbit# 386 Apogee Tracking Contact

@FMI_Setdownlink (40k)

@FMI_SetDownlink (2k)

IBEX Orbit #386 APOGEE Target Vector  11 Nov 17

J2000	Spin Axis

ECI X	-0.708007

ECI Y	-0.648819

ECI Z	-0.278855

Precession Maneuver

MPS Diff	0.759	deg

*MPS Diff should be < 1.5*

0.72995900	ActNor.EstInrToBdy[0]

0.32647700	ActNor.EstInrToBdy[1]

-0.56976000	ActNor.EstInrToBdy[2]

0.18959400	ActNor.EstInrToBdy[3]

1194400000.000	ActNor.EstTime

Right Ascension - RA	222.502	deg

Declination - DEC	-16.192	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	-3.953	deg

MPS Generated Target Vectors

Sun Angle	-0.704904000

MPS Cmd Vector Y	-0.646605000

MPS Cmd Vector Z	-0.291570000

CSS Angle TLM	0.39017

CSS Sun-Pointing Angle	0.78034

05 Nov 17 @0900

CSS Angle TLM	0.972168

CSS Sun-Pointing Angle	1.944336

11 Nov 17 @0200

Pre-Burn

Thruster 1	5648	05 Nov 17 @0900

Thruster 2	5520

Thruster 3	6272

Thruster 4	6400

Post-Burn

Thruster 1	5840	11 Nov 17 @0200

Thruster 2	5712

Thruster 3	6464

Thruster 4	6592

Number of Pulses

Thruster 1	192

Thruster 2	192

Thruster 3	192

Thruster 4	192

Thruster Pairs

Thruster 1 & 2	384

Thruster 3 & 4	384