IBEX Goat Herder  2 Dec 17

The Perigee contacts for Orbit# 388 were nominal for command/telemetry and the sun maneuver successful.

The Star Tracker Reset/Power cycled on 1 Dec 17 (22:59:29 – 23:03:29) UTC during a long star tracker outage (28 Nov @1628 – 2 Dec @1830). Standing CAR# 344 was executed to reset the FDC Response latches and totals.

The star tracker sensor telemetry was also changed for the upcoming ISN season

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, December 02, 2017	336	1500	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	944	344	11 desc	160ksps	182 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1901	2	1292	0	20765	0

VC 2 Write Pointer Start	1157	VC 2 Write Pointer End	6536

VC 2 Read Pointer Start	45932	VC 2 Read Pointer End	6500

Orbit# 388 SSR_Dump/Tracking Contact

@FMI_SetDownlink(320ksps)

reset_master_timer.scr

SSR_Dump.scr (new_RESET_PNTRS_6500)

CAR# 944 Upload Orbit# 390 ATS 1.IBEX_2017_346_o0390a_v001.scr(460-550)

CAR# 344 Reset FDC Totals and Response Latch Valves (star tracker power cycled)

1. @ACT_ResetRespReqLatch(AC_FDC,FDC_STA,FDC_STA_STATETEST)

2. @ACT_ResetRespReqLatch(AC_FDC,FDC_STA,FDC_NOSOLUTIONTEST)

3. @ACT_TesetTaskRawFailed(AC_FDC)

ops_set_sc_time.scr

@FTG_DumpBAckorbit(from start 0,0,0,0)

IBEX Orbit# 388 PERIGEE Target Vectors  2 Dec 17

CSS Angle TLM	2.15277

CSS Sun-Pointing Angle	4.30554

30 Nov 17 @2346

CSS Angle TLM	0.193827

CSS Sun-Pointing Angle	0.387654

2 Dec 17 @1500

Pre-Burn

Thruster 1	7008	30 Nov 17 @2346

Thruster 2	6832

Thruster 3	7712

Thruster 4	7888

Post-Burn

Thruster 1	7328	2 Dec 17 @1500

Thruster 2	7152

Thruster 3	8160

Thruster 4	8336

Number of Pulses

Thruster 1	320

Thruster 2	320

Thruster 3	448

Thruster 4	448

Thruster Pairs

Thruster 1 & 2	640

Thruster 3 & 4	896

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Saturday, December 02, 2017	336	2130	AUWA	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	945	10 asc	320ksps	140 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1049	1	0	0	0	0

VC 2 Write Pointer Start	6667	VC 2 Write Pointer End	6682

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	6500

Orbit# 388 IBEX_Lo Star Sensor Cad. Contact/

CAR# 945 Change star sensor telemetry rate to ISN season rate

1. %constraint off

2. %conversion off

3. @CEU_SET_PARAMETER 4, 123

4.%conversion on

5. %constraint on

6. @CEU_SET_PARAMETER 4, LO_STAR_HISTO_CADENCE

7. @CEU_SET_PARAMETER 123, ROUND_ROBIN_START

8. @CEU_SET_PARAMETER 123, ROUND_ROBIN_END

9.  @CEU_SET_PARAMETER 3, ROUND_ROBIN_START

10. @CEU_SET_PARAMETER 3, ROUND_ROBIN_END

11. @CEU_SET_PARAMETER 0, ROUND_ROBIN_START

12. @CEU_SET_PARAMETER 128, ROUND_ROBIN_END

stx,off