IBEX Goat Herder  12 Dec 17

The Perigee contacts for Orbit# 389 were nominal for command/telemetry and the inertial maneuver successful.

The sweep tables for the Hi Background Test and the Lo ISN Season were successfully loaded.

The Hi Background Test will run for one orbit - the Hi normal sweep table will be reloaded on December 20.

IBEX_Lo will use the ISN Season sweep table until the start of orbit 400 (March 12) except for during arc a of orbit 394 (between January 16 and 21) when we will revert to the Lo normal sweep table

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Monday, December 11, 2017	345	0930	USHI02	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	946	17 desc	160ksps	185 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1082	0	1288	0	0	0

VC 2 Write Pointer Start	33233	VC 2 Write Pointer End	33353

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	6500

Orbit# 389

CAR#946 IBEX_Hi Background Test & IBEX_Lo ISN Sweep Table Upload

1.@CEU_Mode(HVENG)

2.@CEU_Mode(HVSTANDBY) 3.sweep_table_uplaod_160922.scr(Table_Hi_023456_Background,Table_Lo_11223678_ISN,quit)

4.@CEU_Mode(HVENG)

5. @CEU_Mode(HVSCI)

@FTG_DumpBAckorbit,(from start,0,0,0,0)

stx,off

Date	Jday	Time 	Station	Razor#	USNPR#	PASS/FAIL

Tuesday, December 12, 2017	346	0600	USAK	Pass

Controller	CAR1	CAR2	CAR3	Radius Earth	S-Band Rate	Station PWR

SWesley	947	11 asc	320ksps	200 watts

EBNO Values	EBNO Values 3	AGC Strength

EBNO Values 2	AGC Strength 2

VC 0	VC 0 Seq Err	VC 1	VC 1 Seq Err 	VC 2	VC 2 Seq Err

1904	3	0	0	27662	1

VC 2 Write Pointer Start	34261	VC 2 Write Pointer End	34298

VC 2 Read Pointer Start	6500	VC 2 Read Pointer End	34263

Orbit# 389 SSR_Dump/Tracking Contact

reset_master_timer.scr

SSR_Dump.scr(new)

CAR# 947 Upload Orbit# 391 ATS 1.IBEX_2017_355_o0391a_v001.scr(643-734)

IBEX Orbit# 389 PERIGEE Target Vectors  12 Dec 17

J2000	Spin Axis

ECI X	-0.161570

ECI Y	-0.905599

ECI Z	-0.392156

Precession Maneuver

MPS Diff	0.707	deg

*MPS Diff should be < 1.5*

0.38686800	ActNor.EstInrToBdy[0]

-0.73919600	ActNor.EstInrToBdy[1]

0.43594900	ActNor.EstInrToBdy[2]

0.33744700	ActNor.EstInrToBdy[3]

1197090000.000	ActNor.EstTime

Right Ascension - RA	259.884	deg

Declination - DEC	-23.089	deg

IBEX Spin Axis vs. Sun Vector

IBEX Sun Angle	0.333	deg

MPS Cmd Vector X	-0.155422000

MPS Cmd Vector Y	-0.902240000

MPS Cmd Vector Z	-0.402251000

CSS Angle TLM	3.36272

CSS Sun-Pointing Angle	6.72544

11 Dec 17 @1022

CSS Angle TLM	0.68557

CSS Sun-Pointing Angle	1.37114

12 Dec 17 @0600

Pre-Burn

Thruster 1	7648	11 Dec 17 @1022

Thruster 2	7472

Thruster 3	8512

Thruster 4	8688

Post-Burn

Thruster 1	8048	12 Dec 17 @0600

Thruster 2	7872

Thruster 3	8928

Thruster 4	9104

Number of Pulses

Thruster 1	400

Thruster 2	400

Thruster 3	416

Thruster 4	416

Thruster Pairs

Thruster 1 & 2	800

Thruster 3 & 4	832